## Slide 1: SCHLICHTING – TRUCKENBRODT AERODYNAMICS OF THE AIRPLANE
A CRITICAL REVIEW OF CHAPTER TWO: AIRFOIL OF INIFINITE SPAN IN INCOMPRESSIBLE FLOW

## Slide 2: 2D FLOW
THE FLOW ABOUT AN AIRFOIL OF INFINITE LENGTH IS TWO-DIMENSIONAL.
INCORRECT: THE FLOW IS 3D

## Slide 3: LIFT VS CIRCULATION
LIFT PRODUCTION OF AN AIRFOIL IS CLOSELY RELATED TO THE CIRCULATION OF ITS VELOCITY IN THE NEAR-FIELD.
INCORRECT: THERE IS NO DEFINITE RELATION BETWEEN LIFT AND CIRCULATION

## Slide 4: LIFT BY CIRCULATION

## Slide 5: LOWER PRESSURE ABOVE
THERE IS HIGHER PRESSURE ON THE LOWER SURFACE, LOWER PRESSURE ON THE UPPER SURFACE.
IT FOLLOWS THEN FROM BERNOULLI THAT THE VELOCITIES ON THE LOWER AND UPPER SURFACE ARE LOWER AND HIGHER THAN THE VELOCITY OF THE INCIDENT FLOW.
TRIVIALITY: LIFT FROM PRESSURE DIFFERENCE

## Slide 6: LIFT FORMULA
THE LIFT L IS GIVEN BY THE KUTTA-ZHUKOVSKY FORMULA:
L = CONSTANT x CIRCULATION
IF THE CIRCULATION IS KNOWN THE KZ FORMULA IS OF PRACTICAL VALUE FOR THE CALCULATION OF LIFT.
DANGEROUS: DOES NOT PREDICT STALL

## Slide 7: CIRCULATION DETERMINED BY SHARP TRAILING EDGE
EXPERIENCE SHOWS THAT A CIRCULATION FORMS OF THE MAGNITUDE THIS IS NECESSARY TO PLACE THE REAR STAGNATION POINT EXACTLY ON THE SHARP TRAILING EDGE.
NO THEORY: FREE SPECULATION

## Slide 8: CIRCULATION DETERMINED BY SEPARATION AT SHARP TRAILING EDGE

## Slide 9: STARTING VORTEX
BECAUSE OF FRICTION A VORTEX FORMS AT THE TRAILING EDGE WHICH QUICKLY DRIFTS AWAY FROM THE WING AND REPRESENTS THE SO-CALLED STARTING VORTEX.
SINCE THE CIRCULATION REMAINS CONSTANT FOR ALL TIMES ACCORDING TO THE THOMSON THEOREM, THERE MUST BY A CIRCULATION AROUND THE WING EQUAL TO THE STARTING VORTEX.
INCORRECT: CIRCULATION NOT CONSTANT IN TURBULENT FLOW

## Slide 10: VISCOSITY
THE VISCOSITY OF THE FLUID, AFTER ALL, CAUSES THE FORMATION OF CIRCULATION AND THEREFORE THE ESTABLISHMENT OF LIFT.
NO REASON: VISCOSITY NOT ORIGIN OF LIFT

## Slide 11: STARTING VORTEX GENERATED BY VISCOSITY

## Slide 12: SUMMARY: LIFT BY CIRCULATION
NO THEORY
NO RATIONALE
EVIDENCE BY OBSERVATION ONLY SPECULATION

## Slide 13: INCORRECT PRESSURE AT TRAILING EDGE